## Slide 1: FSM with Output

## Slide 2: Content
Definition of Moore Machine
Definition of Mealy Machine
Examples

## Slide 3: FSM with Output
DFA and NFA are machines which specifies output 'YES' or 'NO' by reaching to Final State or Non-Final State respectively
Sometimes it is necessary to specify output other than Yes or No
Hence we have Finite Automata with output
There are two types of Machines:
    Moore Machine
    Mealy Machine

## Slide 4: Moore Machine
Next state is decided by Current State and Current input symbol
The Output symbol depends only on Present State of the machine
Formal Definition:
M = ( Q , Σ , Δ , δ , λ, q0 )
Where Q is a finite set of internal states
Σ is a finite set of symbols called the input alphabet
Δ is Output Alphabet
δ : Q X Σ → Q is a Transition Function (State Function)
q0 is an initial state q0 ε Q
λ : Q → Δ is a output Function

## Slide 5: Moore Machine
Given Moore Machine can be described as
M = ( { q0, q1, q2 }, { 0, 1 }, { 0, 1 }, δ , λ, q0 )
Transition Table:
q0 / 1
q1 / 1
q2 / 0
0
1
0
0
1
1
Current State | Input 0 | Input 1 | Output λ
q0 | q1 | q2 | 1
q1 | q2 | q1 | 1
q2 | q2 | q0 | 0
Output Function:
λ ( q0 ) = 1
λ ( q1 ) = 1
λ ( q2 ) = 0

## Slide 6: Moore Machine
Given Moore Machine can be described as
M = ( { q0, q1, q2 }, { 0, 1 }, { 0, 1 }, δ , λ, q0 )
Transition Function ( δ ):
δ ( q0 , 0 ) = q1 δ ( q0 , 1 ) = q2
δ ( q1 , 0 ) = q2 δ ( q1 , 1 ) = q1
δ ( q2 , 0 ) = q2 δ ( q2 , 1 ) = q0
If the length of the input string is n
Then the length of output string is n + 1
For given machine if input is: 0 1 1 0
Then output is: 1 1 1 1 0
q0 / 1
q1 / 1
q2 / 0
0
1
0
0
1
1

## Slide 7: Mealy Machine
The Output symbol depends on Present State and Present Input Symbol of the machine
Formal Definition:
M = ( Q , Σ , Δ , δ , λ, q0 )
Where Q is a finite set of internal states
Σ is a finite set of symbols called the input alphabet
Δ is Output Alphabet
δ : Q X Σ → Q is a Transition Function (State Function)
q0 is an initial state q0 ε Q
λ : Q X Σ → Δ is a output Function

## Slide 8: Mealy Machine
Given Mealy Machine can be described as
M = ( { q0, q1, q2 }, { 0, 1 }, { 0, 1 }, δ , λ, q0 )
Transition Table:
q0
q1
q2
1 / 0
0 / 0
1 / 1
0 / 0
1 / 0
0 / 1
Current State | Input 0 |  | Input 1 | 
 | State | Output | State | Output
q0 | q2 | 1 | q1 | 0
q1 | q1 | 0 | q2 | 1
q2 | q2 | 0 | q0 | 0
Output Function:
λ ( q0 , 0 ) = 1 λ ( q0 , 1 ) = 0
λ ( q1, 0 ) = 0 λ ( q1 , 1 ) = 1
λ ( q2, 0 ) = 0 λ ( q2 , 1 ) = 0

## Slide 9: Examples on Moore Machine
Ex. 1 Design a Moore machine to generate 1's complement of given binary number
Solution:
For 1's complement if input is 0 then output will be 1.
If input is 1 then output will be 0.
Transition Diagram for Moore Machine can be drawn as
q0 / 0
q1 / 1
q2 / 0
0
0
1
1
1
0
Current State | Input 0 | Input 1 | Output λ
q0 | q1 | q2 | 1
q1 | q1 | q2 | 1
q2 | q1 | q2 | 0
Transition Table:
Above FSM can be represented as
M = ( Q , Σ , Δ , δ , λ, q0 )
Where Q = { q0, q1, q2 }
Σ = { 0, 1 }
Δ = { 0, 1 }
q0 = q0
δ and λ are shown in transition table

## Slide 10: Examples on Moore Machine
Ex. 1 Design a Moore machine to generate 1's complement of given binary number
Solution:
Simulation for the input: 1 1 0 1
q0 / 0
q1 / 1
q2 / 0
0
0
1
1
1
0
Input | 
State | q0
Output | 0
1
q2
0
1
q2
0
0
q1
1
1
q2
0

## Slide 11: Examples on Moore Machine
Ex. 2 Design a Moore machine for binary number input sequence such that if it has a substring 101 then machine outputs A, if input has substring 110, it outputs B, otherwise it gives output C
Solution:
Partial Transition Diagram for Moore Machine can be drawn as
q0 / C
q1 / C
q2 / C
1
1
q3 / A
q4 / C
q5 / B
0
0
1

## Slide 12: Examples on Moore Machine
Ex. 2 Design a Moore machine for binary number input sequence such that if it has a substring 101 then machine outputs A, if input has substring 110, it outputs B, otherwise it gives output C
Solution:
Transition Diagram for Moore Machine can be drawn as
q0 / C
q1 / C
q2 / C
1
1
q3 / A
q4 / C
q5 / B
0
0
1
0
0
0
1
1
0
1
State/ Input | 0 | 1 | Output λ
q0 | q0 | q1 | C
q1 | q2 | q4 | C
q2 | q0 | q3 | C
q3 | q2 | q4 | A
q4 | q5 | q4 | C
q5 | q0 | q3 | B
Transition Table:

## Slide 13: Examples on Moore Machine
Ex. 2 Design a Moore machine for binary number input sequence such that if it has a substring 101 then machine outputs A, if input has substring 110, it outputs B, otherwise it gives output C
Solution:
Transition Diagram for Moore Machine can be drawn as
q0 / C
q1 / C
q2 / C
1
1
q3 / A
q4 / C
q5 / B
0
0
1
0
0
0
1
1
0
1
Above FSM can be represented as
M = ( Q , Σ , Δ , δ , λ, q0 )
Where Q = { q0, q1, q2, q3, q4, q5 }
Σ = { 0, 1 }
Δ = { A, B, C }
q0 = q0
δ and λ are shown in transition table

## Slide 14: Examples on Moore Machine
Ex. 2 Design a Moore machine for binary number input sequence such that if it has a substring 101 then machine outputs A, if input has substring 110, it outputs B, otherwise it gives output C
Solution:
Simulation for String: 1 0 1 1 0 0
q0 / C
q1 / C
q2 / C
1
1
q3 / A
q4 / C
q5 / B
0
0
1
0
0
0
1
1
0
1
Input | State | output
 | q0 | C
1 | q1 | C
0 | q2 | C
1 | q3 | A
1 | q4 | C
0 | q5 | B
0 | q0 | C

## Slide 15: Examples on Mealy Machine
Ex. 3 Design a Mealy machine to generate 2's complement of given binary number
Solution:
For designing 2's complement of binary number, we assume that input is read from LSB to MSB
Suppose Given Number is 1 0 1 1
2's complement: 0 1 0 1
Suppose Given Number is 1 0 1 0
2's complement: 0 1 1 0
We can observe that to get output
We keep binary input as it is until we read first 1
Keep that 1 as it is and then change remaining 1's by 0's and 0's by 1's
Transition Diagram can be drawn as
q0
q1
1 / 0
0 / 1
0 / 0
1/ 1

## Slide 16: Examples on Mealy Machine
Ex. 3 Design a Mealy machine to generate 2's complement of given binary number
Solution:
q0
q1
1 / 0
0 / 1
Transition Table:
Above FSM can be represented as
M = ( Q , Σ , Δ , δ , λ, q0 )
Where Q = { q0, q1 }
Σ = { 0, 1 }
Δ = { 0, 1 }
q0 = q0
δ and λ are shown in transition table
0 / 0
1/ 1
Current State | Input 0 |  | Input 1 | 
 | State | Output | State | Output
q0 | q0 | 0 | q1 | 1
q1 | q1 | 1 | q1 | 0

## Slide 17: Examples on Mealy Machine
Ex. 3 Design a Mealy machine to generate 2's complement of given binary number
Solution:
Simulation for the input: 1 0 1 1
q0
q1
1 / 0
0 / 1
0 / 0
1/ 1
Input | 
State | q0
Output | 
1
q1
1
1
q1
0
0
q1
1
1
q1
0

## Slide 18: Examples on Mealy Machine
Ex.4 Design a Mealy machine to increment given binary number by 1
Solution:
For designing incrementor of binary number, we assume that input is read from LSB to MSB
Suppose Given Number is 1 0 1 1
Resultant Number: 1 1 0 0
Suppose Given Number is 1 1 0 1
Resultant Number: 1 1 1 0
We can observe that to get output
We invert each binary input '1' until we read first 0
Once we get first 0 we will replace it by 1 and then keep remaining bits as it is
Transition Diagram can be drawn as
q0
q1
0 / 0
1/ 1
1/ 0
0 / 1

## Slide 19: Examples on Mealy Machine
Ex.4 Design a Mealy machine to increment given binary number by 1
Solution:
q0
q1
0 / 0
1/ 1
1/ 0
0 / 1
Current State | Input 0 |  | Input 1 | 
 | State | Output | State | Output
q0 | q1 | 1 | q0 | 0
q1 | q1 | 0 | q1 | 1
Above FSM can be represented as
M = ( Q , Σ , Δ , δ , λ, q0 )
Where Q = { q0, q1 }
Σ = { 0, 1 }
Δ = { 0, 1 }
q0 = q0
δ and λ are shown in transition table

## Slide 20: Examples on Mealy Machine
Ex.4 Design a Mealy machine to increment given binary number by 1
Solution:
Simulation for the sting : 1 0 1 1
q0
q1
0 / 0
1/ 1
1/ 0
0 / 1
Input | 
State | q0
Output | 
1
q0
0
1
q0
0
0
q1
1
1
q1
1

## Slide 21: Examples
Ex.1 The Moore machine to determine residue mod 3 for binary number is given.
q0 / 0
q1 / 1
q2 / 2
0
1
1
0
1
0
Transition Diagram can be drawn as above
If we have original no 'n' and we put 0 at the right side of it then value become 2n
If we have original no 'n' and we put '1' at the right side of it then value become 2n+1
Solution:
There will be three states representing the remainder
q0 represents state with remainder 0
q1 represents state with remainder 1
q2 represents state with remainder 2

## Slide 22: Examples
Ex.1 The Moore machine to determine residue mod 3 for binary number is given.
Current State | Input 0 | Input 1 | Output λ
q0 | q0 | q1 | 0
q1 | q2 | q0 | 1
q2 | q1 | q2 | 2
q0 / 0
q1 / 1
q2 / 2
0
1
1
0
1
0
Transition Diagram can be drawn as above
Above FSM can be represented as
M = ( Q , Σ , Δ , δ , λ, q0 )
Where Q = { q0, q1, q2 }
Σ = { 0, 1 }
Δ = { 0, 1 }
q0 = q0
δ and λ are shown in transition table

## Slide 23: Examples
Ex.1 The Moore machine to determine residue mod 3 for binary number is given.
Current State | Input 0 | Input 1 | Output λ
q0 | q0 | q1 | 0
q1 | q2 | q0 | 1
q2 | q1 | q2 | 2
q0 / 0
q1 / 1
q2 / 2
0
1
1
0
1
0
Simulation for the string: 1010
Input | 
State | q0
Output | 0
1
q1
1
0
q2
2
1
q2
2
0
q1
1

## Slide 24: Examples
Ex.2 Construct Mealy machine for given problem:
For input binary string the output symbol toggle between A and B whenever there is input symbol '1'
Assume that A is initial output symbol
Example:
For input 0101 output will be ABBA
For input 0010 output will be AABB
q0
q1
0 / A
1 / B
1 / A
0 / B
Solution:
State q0 generates output symbol as 'A'
State q1 generates output symbol as 'B'

## Slide 25: Examples
Ex.2 Construct Mealy machine for given problem:
For input binary string the output symbol toggle between A and B whenever there is input symbol '1'
Assume that A is initial output symbol
Example:
For input 0101 output will be ABBA
For input 0010 output will be AABB
q0
q1
0 / A
1 / B
1 / A
0 / B
Current State | Input 0 |  | Input 1 | 
 | State | Output | State | Output
q0 | q0 | A | q1 | B
q1 | q1 | B | q0 | A
Above FSM can be represented as
M = ( Q , Σ , Δ , δ , λ, q0 )
Where Q = { q0, q1} Σ = { 0, 1 }
Δ = { A, B } q0 = q0
δ and λ are shown in transition table

## Slide 26: Examples
Ex.2 Construct Mealy machine for given problem:
For input binary string the output symbol toggle between A and B whenever there is input symbol '1'
Assume that A is initial output symbol
Example:
For input 0101 output will be ABBA
For input 0010 output will be AABB
q0
q1
0 / A
1 / B
1 / A
0 / B
Simulation for the string: 0011
Input | 
State | q0
Output | 
0
q0
A
0
q0
A
1
q1
B
1
q0
A

## Slide 27: Example
Ex. 3 Design a Moore machine to convert each occurrence of substring abb by aba
Solution:
Transition Diagram for Moore Machine can be drawn as
q0 / b
q1 / a
q2 / b
b
a
q3 / a
b
b
a
b
State/ Input | a | b | Output λ
q0 | q1 | q0 | b
q1 | q1 | q2 | a
q2 | q1 | q3 | b
q3 | q1 | q0 | a
Transition Table:
a
a

## Slide 28: Example
Ex. 3 Design a Moore machine to convert each occurrence of substring abb by aba
Solution:
Transition Diagram for Moore Machine can be drawn as
q0 / b
q1 / a
q2 / b
b
a
q3 / a
b
b
a
b
a
a
Above FSM can be represented as
M = ( Q , Σ , Δ , δ , λ, q0 )
Where Q = { q0, q1, q2, q3 }
Σ = { a, b }
Δ = { a, b }
q0 = q0
δ and λ are shown in transition table

## Slide 29: Example
Ex. 3 Design a Moore machine to convert each occurrence of substring abb by aba
Solution:
Simulation for the string: a b b a b a
q0 / b
q1 / a
q2 / b
b
a
q3 / a
b
b
a
b
a
a
Input | State | output
 | q0 | b
a | q1 | a
b | q2 | b
b | q3 | a
a | q1 | a
b | q2 | b
a | q1 | a

## Slide 30: Example
Ex. 4 Give mealy machine to each occurrence of substring 120 to 121 where Σ = { 0, 1, 2 }
Solution:
Transition Diagram for Mealy Machine can be drawn as
q0
q1
q2
0/1
1/1
q3
2/2
0/0
1/1
0/0
1/1
1/1
2/2
0/0
2/2
2/2

## Slide 31: Example
Ex. 4 Give mealy machine to each occurrence of substring 120 to 121 where Σ = { 0, 1, 2 }
Solution:
Transition Diagram for Mealy Machine can be drawn as
q0
q1
q2
0/1
1/1
q3
2/2
0/0
1/1
0/0
1/1
1/1
2/2
0/0
2/2
2/2
Current State | Input 0 |  | Input 1 |  | Input 2 | 
 | State | Output | State | Output | State | Output
q0 | q0 | 0 | q1 | 1 | q0 | 2
q1 | q0 | 0 | q1 | 1 | q2 | 2
q2 | q3 | 1 | q1 | 1 | q0 | 2
q3 | q0 | 0 | q1 | 1 | q0 | 2

## Slide 32: Example
Ex. 4 Give mealy machine to each occurrence of substring 120 to 121 where Σ = { 0, 1, 2 }
Solution:
Transition Diagram for Mealy Machine can be drawn as
q0
q1
q2
0/1
1/1
q3
2/2
0/0
1/1
0/0
1/1
1/1
2/2
0/0
2/2
2/2
Current State | Input 0 |  | Input 1 |  | Input 2 | 
 | State | Output | State | Output | State | Output
q0 | q0 | 0 | q1 | 1 | q0 | 2
q1 | q0 | 0 | q1 | 1 | q2 | 2
q2 | q3 | 1 | q1 | 1 | q0 | 2
q3 | q0 | 0 | q1 | 1 | q0 | 2
Above FSM can be represented as
M = ( Q , Σ , Δ , δ , λ, q0 )
Where Q = { q0, q1, q2, q3}
Σ = { 0, 1, 2 }
Δ = { 0, 1, 2 }
q0 = q0
δ and λ are shown in transition table

## Slide 33: Example
Ex. 4 Give mealy machine to each occurrence of substring 120 to 121 where Σ = { 0, 1, 2 }
Solution:
Simulation for the string 1 2 1 2 0 1
Current State | Input 0 |  | Input 1 |  | Input 2 | 
 | State | Output | State | Output | State | Output
q0 | q0 | 0 | q1 | 1 | q0 | 2
q1 | q0 | 0 | q1 | 1 | q2 | 2
q2 | q3 | 1 | q1 | 1 | q0 | 2
q3 | q0 | 0 | q1 | 1 | q0 | 2
Input | State | output
 | q0 | 
1 | q1 | 1
2 | q2 | 2
1 | q1 | 1
2 | q2 | 2
0 | q3 | 1
1 | q1 | 1

## Slide 34: Comparison Between Moore and Mealy Machine
Moore machine
Output: Associated with States
If length of input is n then length of output is ( n + 1 )
Output Function λ : Q → Δ
Example:
Mealy machine
Output: Associated with Transitions
If length of input is n then length of output is also n
Output Function: λ : Q X Σ → Δ
Example:
q0
q1
1 / B
1 / A
0 / B
q0/A
q1/B
1
1
0

## Slide 35: FSM with Output
Applications:
1. Text Editors
- Processing Text
- Uses Regular Expressions for substituting strings
2. Lexical Analysis
- Separate Tokens and recognize them
Limitations
1. Well formedness of Parenthesis
2. Checking palindrome of given language

## Slide 36: Thank You …